## Slide 1: Thermodynamics Design Lab
Design Laboratory Assignment: Atmospheric Satellites Assigned: 19 September 2017 Due: 3 October, Prelab report on balloon scale model results
Due: 16 October, All Presentations due 11:59 PM
Red Bull Stratos Launch Vehicle and Limb of the Earth’s Atmosphere Viewed by Felix Baumgartner from an Altitude of 37 km (~120,000 feet)
http://www.redbullstratos.com/
http://www.rt.com/news/199136-eustace-stratosphere-jump-record/
http://www.bigelowaerospace.com/beam/
http://www.google.com/loon/

## Slide 2: Schedule
Week 1: Prelab. Begin design
Week 2: Finish Pre-lab. Continue design
Week 3: Submit pre-lab. Finalize design
Week 4: Finish design presentation
Week 5: Presentations
  ITLL and Idea Forge
  UPDATE WITH PICTURE FROM ASSIGNMENT

## Slide 3: Red Bull Stratos
Red_Bull_Stratos

## Slide 4: Google’s Project Loon – Atmosphere Satellites
On 16 June 2013, Google began a pilot experiment in New Zealand where about 30 balloons were launched in coordination with the Civil Aviation Authority from the Tekapo area in the South Island. About 50 local users in and around Christchurch and the Canterbury Region tested connections to the aerial network using special antennas. After this initial trial, Google plans on sending up 300 balloons around the world at the 40th parallel south that would provide coverage to New Zealand, Australia, Chile, and Argentina. Google hopes to eventually have thousands of balloons flying in the stratosphere.
In May 2014 Astro Teller announced that rather than negotiate a section of bandwidth that was free for them worldwide they would instead become a temporary base station that could be leased by the mobile operators of the country it was crossing over.
In May-June 2014 Google tested its balloon-powered internet access venture in Piauí, Brazil, marking its first LTE experiments and launch near the equator.

## Slide 5: Thermodynamics Design Pre-Lab
  1.3 Scale Model Balloon System
Prior to developing a design for a high-altitude balloon system, your task is to build a scale model of a zero-pressure balloon and develop a mechanical and thermal assessment of the system.
  1.4 Design a High-Altitude Balloon
In your groups, perform a design analysis of a high-altitude balloon for carrying a research payload.
Your design requirements are as follows:
    1.4.1 Payload. A 500 kg research instrument.
    1.4.2 Altitude. The balloon should be able to reach an altitude of 35 km
    1.4.3 Duration. The balloon should be able to stay in residence for at least one day.
Assumptions:
    1.4.4 Shape. Assume the shape of the balloon at target altitude is a sphere
    1.4.5 Transients. Ignore transient effects during ascent
    1.4.6 Stresses. Ignore stresses on balloon material associated with attaching the payload or wind loading

## Slide 6
Buoyant force: The upward force a fluid exerts on a body immersed in it. The buoyant force is caused by the increase of pressure with depth in a fluid.
A flat plate of uniform thickness h submerged in a liquid parallel to the free surface.
The buoyant force acting on the plate is equal to the weight of the liquid displaced by the plate.
For a fluid with constant density, the buoyant force is independent of the distance of the body from the free surface.
It is also independent of the density of the solid body.

## Slide 7
Archimedes’ principle: The buoyant force acting on a body immersed in a fluid is equal to the weight of the fluid displaced by the body, and it acts upward through the centroid of the displaced volume.
The buoyant forces acting on a solid body submerged in a fluid and on a fluid body of the same shape at the same depth are identical. The buoyant force FB acts upward through the centroid C of the displaced volume and is equal in magnitude to the weight W of the displaced fluid, but is opposite in direction. For a solid of uniform density, its weight Ws also acts through the centroid, but its magnitude is not necessarily equal to that of the fluid it displaces. (Here Ws > W and thus Ws > FB; this solid body would sink.)

## Slide 8
For floating bodies, the weight of the entire body must be equal to the
buoyant force, which is the weight of the fluid whose volume is equal to the
volume of the submerged portion of the floating body:
A solid body dropped into a fluid will sink, float, or remain at rest at any point in the fluid, depending on its average density relative to the density of the fluid.

## Slide 9
The altitude of a hot air balloon is controlled by the temperature difference between the air inside and outside the balloon, since warm air is less dense than cold air. When the balloon is neither rising nor falling, the upward buoyant force exactly balances the downward weight.

## Slide 10: Design a Neutrally Buoyant Balloon System
Neutral Buoyancy = Force Balance
Reduce the force balance equation to one extensive variable, Volume of the balloon, because this is what you want to find and other intensive properties can be looked up without requiring knowledge of the system extent.
NASA Neutral Buoyancy Lab
Archimede’s Principle: The buoyant force of an immersed object equals the weight of the fluid displaced by the object

## Slide 11: Thin-Walled Pressure Vessel
Thickness of the wall is much less than its radius
The normal stress is exerted uniformly throughout the vessel walls.
where Pg is the gage pressure
The ultimate stress of the material (which is a property of a material at which the material fails) given symbolically as su is related to the normal stress by a factor, k, often termed the factor of safety
Two assumptions that apply to a thin-walled pressure vessel

## Slide 12: Design Lab Analysis
The thinned-wall pressure vessel assumption leads to an expression for the thickness that depends on factor of safety, balloon radius, gage pressure and ultimate stress
For the lab assume a gage pressure of 10 pascals,
Let the factor of safety be a variable by which you determine and justify in your presentation
Select a balloon material to find its material density and ultimate stress
Solve for the balloon volume (or equivalently the balloon radius) based on the design requirements
Resources:
NASA Long Duration Balloon Facility
Materials Website : http://www.matweb.com/
Standard atmosphere
  MATLAB Mathworks website, file exchange: function atmoscoesa
  Online standard atmosphere calculator
  Intro to Flight, Chapter 3

## Slide 13: Prelab Tasks
Nation-wide He shortage
  Reuse balloons
  Record empty mass on a sticky note, place on your balloon after lab.
WATER TANK IS LAST!
Make sure to relate the ‘prelab’ to your design.
  This is valuable for senior projects and beyond.